## Slide 1
SMART GLASSES
FOR THE VISUALLY IMPAIRED
Graduation Project • Faculty of Science, Zagazig University
Department of Mathematics | 2025–2026
PREPARED BY
Mohamed Ahmed Ali
Youssef Mohamed Ali Ahmed
Mohamed Essam Hessen
Ehab Amen Mohamed
Nourhan Mohamed Mansour
Aml Yasser Othman Ibrahim
SUPERVISOR
Dr. Zahraa Youssef

## Slide 2
Table of Contents
Project Overview
01
Introduction & Problem Statement
02
Why Python?
03
System Architecture & Flowchart
04
Hardware Components Overview
05
ESP32-CAM & OV3660 Sensor
06
Arduino Nano – Controller
07
Ultrasonic Sensor & Buzzer
08
Power Management System
09
Hardware Connections Summary
10
Software Libraries Overview
11
YOLOv5 Object Detection (Parts 1–3)
12
ESP32-CAM Web Interface
13
GUI Interface
14
Training on Google Colab
15
Results & Conclusion

## Slide 3
Project Abstract
The Challenge We Are Solving
Visual impairment significantly affects the independence and quality of life of blind and visually impaired individuals. This project presents the design and implementation of a smart assistive glasses system aimed at enhancing mobility and environmental awareness through real-time audio feedback.
285M+
People with visual
impairment worldwide
39M
People who are
completely blind
80%
Of visual impairments
are preventable or curable

## Slide 4
Introduction
Chapter 1 – Overview
Navigation Challenge
Daily navigation, reading, and object ID require external help, reducing independence.
Technology Solution
Rapid advancement enables smart assistive wearable devices.
Project Goal
Smart glasses combining obstacle detection (sensors) + text recognition (OCR) + audio feedback.
Key Benefit
Portable, accurate, and easy-to-use – a comprehensive wearable assistant.

## Slide 5
Why Python?
The Core Software Platform
01
Simple Syntax
Easy to understand, develop, and maintain even for complex features.
02
Rich Ecosystem
OpenCV, Tesseract, Pillow, pyttsx3, PyTorch – all available.
03
Real-Time Processing
Handles sensor inputs and camera data simultaneously.
04
Hardware Integration
Strong support for ESP32 via GPIO and serial libraries.
05
Rapid Prototyping
Fast iteration on OCR algorithms and detection systems.
06
Community Support
Large active community, extensive documentation.

## Slide 6
System Architecture
How It All Connects
Camera
(ESP32-CAM)
Ultrasonic
Sensor
Image
Processing
(YOLOv5 / OCR)
Arduino
Nano
Controller
Audio
Feedback
(Speaker)
Buzzer
Alert
System processes visual data in real-time, delivering audio guidance within milliseconds.

## Slide 7
Hardware Components
Complete Bill of Materials
ESP32-CAM
OV3660 camera module + Wi-Fi SoC
Arduino Nano
ATmega328P main controller
HC-SR04
Ultrasonic distance sensor
DFPlayer Mini
MP3 audio playback module
18650 Battery
Rechargeable lithium power source
TP4056
Charging & protection circuit
Boost Converter
5V step-up from 3.7V battery
Buzzer
Proximity audio alert
3W Speaker
Audio output for voice feedback
9V Battery
Secondary power option

## Slide 8
ESP32-CAM Development Board
With OV3660 Image Sensor
Module Overview
The ESP32-CAM is a low-cost, low-power System-on-Chip (SoC) combining a dual-core processor with integrated Wi-Fi and Bluetooth. Paired with the OV3660 sensor, it provides high-fidelity visual data acquisition for the smart glasses system.
Processor:
Xtensa dual-core LX6, up to 240 MHz
RAM:
520 KB SRAM
Flash:
4 MB PSRAM
Wireless:
Wi-Fi 802.11 b/g/n + BT 4.2
GPIO:
Multiple I2C, SPI, UART, ADC, PWM
Power:
Deep sleep: 6 µA
OV3660 Sensor
Resolution
3MP (2048×1536)
Format
JPEG / YUV422
Max FPS
Up to 15 fps @3MP
FOV
66.5° wide angle
Interface
DVP (SCCB)
Voltage
1.5V / 2.8V
Night Mode
Auto exposure

## Slide 9
ESP32-CAM – Key Functions
How It Powers the Smart Glasses
Visual Acquisition
Continuously captures high-resolution images/video of the user's environment.
Wireless Transmission
Uses built-in Wi-Fi to send image payloads to cloud or smartphone via HTTP/HTTPS.
AI & Computer Vision
Enables object detection, OCR, and facial recognition via deep learning models.
Wearable Viability
Ultra-compact footprint + low power consumption – ideal for head-mounted devices.

## Slide 10
ESP32-CAM – Software Setup & Workflow
Arduino IDE + OV3660 Configuration
1
Initialization
System boots and connects to pre-configured Wi-Fi / mobile hotspot automatically.
2
Camera Config
CAMERA_MODEL_AI_THINKER pinout with OV3660 parameters: resolution, JPEG quality, frame rate.
3
Capture
Images captured at time intervals or triggered by user button press.
4
Transmission
Payload sent via HTTP/HTTPS to cloud server or local processing unit.
5
AI Feedback
Cloud/smartphone processes image with AI; audio results routed back to user.
Dev Tools
Arduino IDE
ESP32 Board Package
FTDI Programmer
AI Thinker Pinout
HTTP Client Lib
WiFiClientSecure

## Slide 11
Arduino Nano
ATmega328P – The System Controller
Technical Specifications
Processor:
ATmega328P
Clock Speed:
16 MHz crystal oscillator
Throughput:
16 MIPS at 16 MHz
Flash Memory:
32 KB (2 KB bootloader)
SRAM:
2 KB internal
EEPROM:
1 KB
Voltage:
5V (3.3V limited)
Input Voltage:
7–12V recommended
Digital I/O:
14 pins
Analog Inputs:
8 pins
PWM Outputs:
6 pins
Power:
USB Mini-B / VIN pin
Role in Smart Glasses
Receive Data
Gets object detection results from ESP32-CAM via UART (TX/RX)
Distance Reading
Reads HC-SR04 ultrasonic sensor distance data
Audio Control
Controls DFPlayer Mini to play pre-recorded voice messages
Buzzer Logic
Activates buzzer when object is within 30 cm threshold
Power Managed
Powered by 5V Boost Converter from 18650 battery

## Slide 12
Ultrasonic Sensor & Buzzer
HC-SR04 – Obstacle Detection
HC-SR04 Sensor
Measures distance using Time-of-Flight (ToF) by emitting 40 kHz ultrasonic pulses and measuring the reflected echo. Distance = (Time × Speed of Sound) ÷ 2
Pin Connections
VCC
5V from Arduino
GND
Arduino Ground
TRIG
Digital output pin
ECHO
Digital input pin
Buzzer Alert Logic
Trigger Distance:
≤ 30 cm from obstacle
Signal Type:
Arduino digital HIGH/LOW
Alert Pattern:
Continuous while obstacle present
Type Used:
Active buzzer (no PWM needed)
Power:
5V, shared with Arduino
Code Logic:
if (distance > 0 && distance <= 30) {
digitalWrite(buzzer, HIGH); }
else { digitalWrite(buzzer, LOW); }

## Slide 13
Power Management System
18650 + TP4056 + Boost Converter
18650 Li-Ion Battery
Nominal Voltage: 3.7V
Capacity: ~2500 mAh
Rechargeable lithium-ion cell
Provides portable power
TP4056 Charge Module
Safe CC/CV charging
Over-charge protection
Over-discharge protection
B+/B– to battery terminals
Boost Converter (5V)
Steps 3.7V → stable 5V
Supplies Arduino Nano
Supplies ESP32-CAM
OUT– → common ground
Battery → TP4056 → Boost Converter → Arduino & ESP32

## Slide 14
Hardware Connections Summary
Complete System Wiring
01
ESP32-CAM → Arduino Nano
TX/RX cross-connection for serial data transfer
02
Arduino Nano → Ultrasonic
TRIG=output, ECHO=input, VCC=5V, GND
03
Arduino Nano → Buzzer
Digital pin HIGH/LOW control
04
Arduino Nano → DFPlayer
TX/RX digital pins for audio commands
05
DFPlayer → Speaker
SPK1 / SPK2 direct speaker connection
06
TP4056 → Boost
OUT+/OUT– to boost converter input
07
Boost → Arduino & ESP32
5V OUT+ to both VCC pins
08
Common Ground
All components share GND for stable operation

## Slide 15
Python Software Libraries
The Software Stack
TensorFlow
Deep learning framework by Google for model training & deployment
OpenCV
Real-time image capture, preprocessing and video processing
YOLOv5/v8
Object detection – identifies items in single forward pass
PyTorch
Neural network training & GPU-accelerated inference
pyttsx3
Offline text-to-speech audio feedback generation
SpeechRecognition
Voice command input – hands-free interaction
PIL / Pillow
Image resizing, cropping, color conversion
NumPy
Efficient array/matrix operations for model I/O
Matplotlib
Visualization of training metrics and results
Roboflow
Dataset annotation, augmentation, and management
Tkinter
GUI creation for developer/caregiver interface
Requests
HTTP communication with ESP32-CAM over network

## Slide 16
YOLOv5 Object Detection – How It Works
Part 1 – Architecture & Core Principles
YOLO (You Only Look Once) is a real-time object detection algorithm that treats detection as a single regression problem. Unlike traditional methods that scan the image multiple times with sliding windows, YOLO divides the image into an S×S grid and predicts bounding boxes, confidence scores, and class probabilities all in one forward pass through the neural network — making it dramatically faster than two-stage detectors like R-CNN.
Grid-Based Detection
Image divided into S×S cells. Each cell predicts B bounding boxes + confidence + C class probabilities simultaneously.
Single Forward Pass
No region proposals needed. One CNN pass produces all detections — enables real-time processing even on lightweight hardware.
Bounding Box Regression
Each box predicted as (x, y, w, h, confidence). NMS filters overlapping boxes to keep only the highest-confidence detection.
Anchor Boxes
Pre-defined aspect ratio templates. YOLOv5 uses 3 anchors per scale across 3 detection heads (small, medium, large objects).
Confidence Score
Pr(Object) × IoU(pred, truth). Only detections above threshold (e.g. 0.5) trigger audio announcement to the blind user.
Multi-Scale Detection
YOLOv5 uses FPN (Feature Pyramid Network) to detect objects at 3 different scales — handles both nearby obstacles and far objects.

## Slide 17
YOLOv5 Model Variants & Our Choice
Part 2 – Model Selection for Wearable Deployment
YOLOv5 comes in 5 variants scaling from Nano to XLarge. For smart glasses worn by visually impaired users, we prioritize speed and low memory over maximum accuracy — making YOLOv5 Nano the ideal choice. It runs comfortably via Wi-Fi on the ESP32-CAM with Python inference on the connected PC, achieving real-time performance without GPU hardware.
YOLOv5n (Nano) ✓ Used
1.9M params, ~4.5ms latency. Smallest & fastest — perfect for wearables with limited processing power.
YOLOv5s (Small)
7.2M params, ~6.4ms. Higher accuracy than Nano, still fast. Good alternative if processing allows.
Detection Classes
Trained on COCO (80 classes): person, chair, door, bottle, car, phone, cup, backpack, and more — all relevant to daily life navigation.
Transfer Learning
Pre-trained weights on COCO loaded first, then fine-tuned on our specific dataset. Saves training time and boosts accuracy with fewer images.
Input: 320×320 px
ESP32-CAM streams JPEG frames. Python resizes to 320×320 before feeding to YOLOv5 — balances detail vs speed.
Audio Output Pipeline
Detected class name passed to pyttsx3 TTS engine. 3-sec cooldown prevents repeated announcements for same object.

## Slide 18
Object Detection – Results & Performance
Part 3 – Evaluation Metrics & Real-World Accuracy
Object detection performance is measured using standard metrics: mAP (mean Average Precision), Precision, and Recall. Our YOLOv5 Nano model was evaluated on a held-out validation set after training on Google Colab. Results confirm the model is reliable enough for real-world assistive use, correctly identifying everyday objects with high confidence scores across varied lighting conditions.
Precision: 0.864
86.4% of all detections made by the model are correct. Low false positive rate — model doesn't announce non-existent objects.
Recall: 0.850
85% of real objects in the scene are detected. Low miss rate — critical for safety so blind users aren't left unwarned of obstacles.
mAP@0.5: 92.8%
Mean Average Precision at IoU=0.5. Measures how well bounding boxes overlap real objects — 92.8% is excellent for assistive wearables.
mAP@0.5:0.95: 78.7%
Stricter metric averaged across IoU 0.5–0.95. Confirms model generalises well even under tighter overlap requirements.
IoU Explained
Intersection over Union = overlap area / union area. IoU > 0.5 means predicted box covers at least half the real object — counted as correct.
Real-Time FPS
System achieves 10–15 FPS over Wi-Fi ESP32-CAM stream — sufficient for live obstacle detection and audio alerts in walking scenarios.

## Slide 19
ESP32-CAM Web Interface
Live Camera Streaming Dashboard – Developer & Caregiver Panel
The ESP32-CAM hosts a secure web dashboard accessible via Wi-Fi. A PIN-protected login screen guards access, after which caregivers and developers can monitor the live camera feed, view captured photos, configure settings, and track system activity — all from a browser without any additional software. The interface is built with a dark theme for readability and clarity.
PIN Login Screen
4-digit PIN entry protects the dashboard. Prevents unauthorized access to the camera feed and system controls over the local network.
Live Camera Preview
Real-time MJPEG video stream from the ESP32-CAM shown directly in the browser. Caregiver can see exactly what the glasses see.
Status Dashboard
Top cards show: photos captured count, last capture time, Flash GPIO state (ON/OFF), and photos uploaded to Google Drive — at a glance.
Settings Panel
Toggle switches for: Flash (GPIO 4), Auto Save to Google Drive, HDR Mode (higher quality), and Notifications on capture — all configurable live.
Activity Log
Timestamped event log shows: photo saved to Drive, new capture requests, Flash ON/OFF, and login events — full traceability for debugging.
Capture & Google Drive
One-click capture button triggers the ESP32-CAM. With Auto Save enabled, photos upload automatically to Google Drive for remote access.

## Slide 20
OCR & Text-to-Speech
Reading the World Aloud
Tesseract OCR
Open-source OCR engine that recognizes printed text from images captured by the ESP32-CAM. Reads signs, books, labels, and documents.
pyttsx3 TTS
Offline text-to-speech library. Converts recognized text and object names into spoken audio at 150 wpm, playable through the speaker.
SpeechRecognition
Listens for voice commands from the user, enabling hands-free interaction with the glasses system.
Cooldown System
3-second cooldown prevents repetitive speech when the camera stays pointed at the same object, using a timestamp dictionary.
Threading + Queue
Speech runs in a separate background thread (via queue FIFO) so detection never freezes or lags during voice output.
DFPlayer Mini
Hardware audio module that plays pre-recorded voice messages (e.g., currency values) via serial commands from Arduino Nano.

## Slide 21
Graphical User Interface (GUI)
Python Tkinter – Developer & Caregiver Panel
A Tkinter-based GUI allows developers and caregivers to monitor, test, and configure the smart glasses system without any command-line knowledge.
Live Camera Feed
Displays real-time video from the ESP32-CAM module.
Detection Results
Shows detected objects, confidence scores, and bounding boxes.
Currency Display
Highlights recognized Egyptian banknote denomination.
Start / Stop Controls
Buttons to toggle object detection and scene description.
Voice Test Button
Test the audio output and TTS engine directly from the GUI.
Obstacle Alerts
Visual indicator when ultrasonic sensor detects nearby objects.
Scene Description
AI-generated natural language description of the captured scene.
System Status
Shows connection status, model load state, and Wi-Fi info.

## Slide 22
Training on Google Colab
YOLOv5 Model Training Pipeline
!python train.py --img 320 --batch 16 --epochs 11 --data Egyptian-Currency-2/data.yaml --weights yolov5n.pt --cache
--img 320
Images resized to 320×320 px — reduces computation, ideal for wearables.
--batch 16
Processes 16 images at once — balances speed vs. memory usage.
--epochs 11
Full dataset seen 11 times — sufficient for transfer learning convergence.
--data
data.yaml defines paths, class count, and class names (6 denominations).
--weights yolov5n.pt
YOLOv5 Nano pre-trained weights — enables transfer learning.
--cache
Images cached in RAM — significantly speeds up training iterations.

## Slide 23
Key System Features
What the Smart Glasses Can Do
Real-Time Object Detection
YOLOv5 identifies objects instantly from the ESP32-CAM live feed.
Audio Feedback
pyttsx3 announces detected objects, currency, and alerts via speaker.
Currency Recognition
Identifies all 6 Egyptian banknote denominations (5–200 EGP).
Voice Interaction
Hands-free voice commands for controlling detection and navigation.
Obstacle Detection
HC-SR04 ultrasonic sensor warns user when objects are within 30 cm.
Wireless Connectivity
ESP32 Wi-Fi module connects to cloud or smartphone for AI processing.
Lightweight & Wearable
Compact hardware design minimizes weight for daily comfort.
GUI Interface
Tkinter GUI for caregivers to monitor system and configure settings.

## Slide 24
Arduino Code – Logic Overview
Ultrasonic Measurement & Buzzer Control
Code Structure
Pin Definitions:
trigPin, echoPin, buzzer declared as const int.
setup():
pinMode configurations + Serial.begin(9600).
TRIG Pulse:
LOW→HIGH for 10µs to trigger ultrasonic pulse.
ECHO Reading:
pulseIn() measures round-trip echo duration.
Distance Calc:
distance = (duration × 0.0343) / 2 (cm).
Serial Output:
Prints distance to Serial Monitor for debugging.
Buzzer Logic:
if (distance > 0 && distance <= 30) → HIGH.
Loop Delay:
delay(50ms) for measurement stability.
Applications
Obstacle detection
Smart walking aids
Assistive wearables
Safety alert systems
Distance monitoring
Robotic navigation

## Slide 25
What Are Smart Glasses?
Defining Our Assistive System
A wearable device with intelligent hardware & software — captures visual data, processes it with AI, and delivers audio guidance to blind users in real time.
Automation:
Auto-detects objects, obstacles, and currency without user input.
Connectivity:
Integrates Python, Arduino/ESP32, camera, and audio seamlessly.
User Interaction:
Voice commands + audible responses — fully hands-free.
Safety:
Ultrasonic obstacle detection reduces accident risk.
Accessibility:
All interactions via audio; no vision required to operate.
Adaptability:
Responds dynamically to lighting changes and varied environments.
Convenience:
Lightweight wearable design for everyday daily activities.
Future-Ready:
Expandable: GPS, facial recognition, IoT, embedded AI platforms.

## Slide 26
Conclusion & Results
Project Outcomes
The smart glasses system effectively assists visually impaired users in obstacle detection and text/currency recognition. Experimental results confirm reliable real-time performance with high detection accuracy and clear audio responses.
92.8%
mAP@0.5
78.7%
mAP@0.5:0.95
0.864
Precision
0.850
Recall
Future Enhancements
GPS-based outdoor navigation & path planning
Enhanced multi-sensor obstacle detection with data fusion
Larger deep learning dataset for improved recognition
Full IoT integration with smartphone & cloud
Embedded AI deployment (Jetson Nano, RPi)
Multilingual text-to-speech support

## Slide 27
Thank You
Smart Glasses for the Visually Impaired
Prepared by:
Mohamed Ahmed Ali Youssef Mohamed Ali Ahmed
Mohamed Essam Hessen Ehab Amen Mohamed
Nourhan Mohamed Mansour Aml Yasser Othman Ibrahim
Supervisor: Dr. Zahraa Youssef
Faculty of Science, Zagazig University | Department of Mathematics | 2025–2026